## Slide 1: ITU-ML5G-PS-014: Build-a-thon(PoC)
Team: Automato
Mehmet Karaca & Doruk TaylI & Özge simay demirci 30 Nov 2021
HOST: ITU Focus Group Autonomous networks (FG-AN)

## Slide 2: Problem Definition
Make resource allocation decision for
emergency slice İn an autonomous way:
    Get & parse high-level intent
      Requirements for ES
      Information regarding data, ML models
    Make traffic analysis
    Admission & priority control
    Make resource allocation

## Slide 3: Building Blocks
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation
Closed-loop

## Slide 4: Intent Parsing
We get intent from higher-loop (Open-RAN NonRT-RIC).
Indicates if there is an emergency case and monitoring xApp is triggered.
  Information about where data and ML models are.
Intent is created by another team in this Challenge.
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation

## Slide 5: Traffic Forecasting
We monitor RAN resource utilization
  Checks for available PRBs for emergency slice
  We apply Gaussian Process Regression (GPR) for time-series forecast of PRB utilization
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation

## Slide 6: Traffic Forecasting (cont)
  We develope this building block as a RIC xApp. This is our first xApp for this problem.
  Real data (PRB utilization) taken from paper [1].
PRB utilization of a given slice
Upper bound for
the prediction over W samples
used for training (last P samples)
[1] Vaclav Raida , Philipp Svoboda, Markus Rupp : “Real World Performance of LTE Downlink in a Static Dense Urban Scenario - An Open Dataset “ , IEEE GLOBECOM 2020.

## Slide 7: Priority Control
  RAN is shared with other possible slices that have certain number of PRBs dedicated to them. How much resource should we allocate to emergency slice (ES)?
  Level of emergency
    Protect the excisting slices first (ES is the second priority)
      Algorithm 1 (ALG 1)
    Always give the first priority to ES
      Algorithm 2 (ALG 2)
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation

## Slide 8: Resource Allocation
  ALG 1 and ALG 2 decide on resource allocation
    How many PRB should we allocate for ES?
  Resource Allocation block is impelemtned as RIC xApp. This is our second RIC xApp.
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation

## Slide 9: ALG 1
Resource allocation
(ALG 1)
For each other slice n
Step 1: Train GPR with the latest P training data
Step 2: Forecast PRB utilization over the next W samples with GPR -> Un
Step 3: Calculate maximum possible PRB utilization-> Cn = Un + on
Step 4: Calculate forecasted PRB usage over next W samples -> Bn = TnCn
End
Step 5: Calculate available PRBs for Emergency Slice ->PES = T -
Step 6: Allocate PRBs to ES -> PES
Example: Two slices
Total system PRBs = 100
Amoun of PRBs allocated to first slice is 40, utilization is %80 (predicted)-> 8 PRBs unused
Amoun of PRBs allocated to second slice is 60, utilization is %90 (predicted)-> 6 PRBs unused
PRBs allocated to emergency slice is 8 +6 = 14 PRBs
IDEA: Amount of PRBs allocated to other slices are not always used (underutilization). Predict unused PRBs of other slices (leftover from other network slices) and allocate them to ES.

## Slide 10: ALG 2
Resource allocation
(ALG 2)
IDEA:Emergency slice needs E amount of PRBs (fixed). Allocate the available PRBs to ES first. If it is not enough borrow PRBs from other slices. Aim is to always give E PRBs to ES. ES has the first priority.
[3] Armin Okic, Lanfranco Zanzi, Vincenzo Sciancalepore, Alessandro Redondi, Xavier Costa-Pérez, “ π-ROAD: a Learn-as-You-Go Framework for On-Demand Emergency Slices in V2X Scenarios “, IEEE INFOCOM, 2020.
[2] X. Foukas et al., “Orion: RAN Slicing for a Flexible and Cost-Effective Multi-Service Mobile Network Architecture,” in ACM MobiCom, 2017.
Solve an optimization problem:
min
s.t.
PRB needed for slice n at time t
Number of PRB taken from slice n at time t to be used for emergency slice
Guarantee that emergency slice gets enough PRBs
We damage slice n this amount by taking PRBs from it
Total PRBs given to slice n
Transform this problem to a solvable integer problem

## Slide 11: ALG 2 (cont)
Resource allocation
(ALG 2)
IDEA: Emergency slice needs E amount of PRBs (fixed). Allocate the available PRBs to ES first. If it is not enough borrow PRBs from other slices. Aim is to always give E PRBs to ES. ES has the first priority.
Solve an integer programming using auxiliary variable :
min
) (t) +
Actual PRB usage at time t in future.
This cannot be known in advance
Estimated PRB usage with GPR
Estimation error.
Upper bound can be used provided by GPR.
We have implemented ALG1 & ALG2 and next we will show a demo for ALG2

## Slide 12: Experiment: resource allocation
Two other slices:
  40 and 60 PRBs allocated these two slices
  The network has 100 PRBs (ES should borrow from others)
Emergence slice needs E = 20 PRBs
Result from the Figure: at every decision-time,
sum of these PRBs is always 20, which ES needs.

## Slide 13: ML model selection for forecasting
Different ML models with different performance, comlexity and cost can be available in a pool.
We implement this scheme as a microservice (docker).
  Webserver stores different ML model
  Possible to fetch a differebt ML model when forevasting
İnten parsing
(.json)
Traffic Forcasting
Admission & Priority control
Resource Allocation
ML Model Selection
Slice information & requirements
PRB utilization
Slice admission and priority
Different ML models in a pool
PRB allocation

## Slide 14: Our implementation
src
C
M1
sink
ML pipeline
RAN
We have developed and implemented RIC xApp1, xApp2 and server as a microservice.
These xApps can communicate through a RIC (O-RAN messaging) message.
  e.g., xApp1 can send prediction to xApp2 over the network

## Slide 15: Demo
We have a quick demo:
Ubuntu 20.04 Works fine
Need docker and docker compose
Check for details: https://github.com/ITU-AI-ML-in-5G-Challenge/ITU-ML5G-PS-014-Build-a-thon-PoC---Team-AUTOMATO-

## Slide 16: Conclusion and Future Works
A PoC for autonomous slice management
Resource allocation handled with an autonomous closed-loop
Machine learning and ML module are crucial
Flexible and modular O-RAN RIC xApps design
  Future Works:
Integration of all xApps to testbed, real O-RAN infrastructure
Other optimizations & improvements
Dynamic estimation of emergency slice
This work has been supported by Scientific and Technological Research Council of Turkey (TÜBİTAK, grant no. 120E485)

## Slide 17
Thank you for listening!
Q & A
mehmet.karaca@tedu.edu.tr
doruktayli@gmail.com
osimay.demirci@tedu.edu.tr